## Slide 1: Presentation of the Synthesis Project
Chiheb BEN DAHSEN
Fares FRIKHA
Mariem HAJJI
Année universitaire 2020-2021
National Engineering School of Tunis
University of Tunis El Manar
Civil Engineering Department
3 Year Civil Engineering 2
Development and study of a complete interchange

## Slide 2: LAYOUT
Introduction
Bibliographic study
Traffic study and layout propositions
Pavement dimensioning
Modeling the bridge using “SAP2000”
Conclusion

## Slide 3: INTRODUCTION
In order the minimize the traffic jam in Tunis, we have to make:
An Interchange

## Slide 4: BIBLIOGRAPHIC STUDY
Definitions
Types of interchanges

## Slide 5: Definition
An interchange is a road junction that uses grade separation and typically one or more ramps to permit traffic on at least one highway to pass through the junction without interruption from other crossing traffic streams.

## Slide 6: Types of interchanges
Service Interchanges
Diamond Interchange
Cloverleaf Interchange
Partial Cloverleaf interchange
Roundabout Interchange

## Slide 7: Types of interchanges
System Interchanges
Directional Interchange
Cloverstack Interchanges
Turbine Interchange

## Slide 8: TRAFFIC STUDY AND LAYOUT PROPOSITIONS
Traffic data
Justification of the layout
Design stages
Layout prepositions

## Slide 9: Traffic data
01
02
03
04
Project’s commission year : 2022
Lifetime : 20 years.
Annual growth rate : 3%.
Width of a track : 3,5 m.

## Slide 10: Traffic data
2017
2042

## Slide 11: Justification of the layout
Daily p.v.u traffic in commissioning year 2022
  The maximum average daily traffic in terms of heavy goods vehicles in 2017 : T2017 = 1922 pvu/peak hour
  The maximum average daily traffic in terms of heavy goods vehicles in 2022 : T2022 = 2229 pvu/peak hour
Daily p.v.u traffic at end of service year 2042
Determination of the number of lanes
2x3 lanes for X20 and X3
1 lane for suspenders and curls

## Slide 12: Design stages
Importing crossroads from Google Earth
Drawing the bridges
Drawing the roads X20 and X3
Drawing the piers, abutments and bearings
Drawing curls
Drawing the suspenders

## Slide 13: Layout propositions
Layout proposed by Mariem
Layout proposed by Fares
Layout proposed by Chiheb

## Slide 14: PAVEMENT DIMENSIONING
Dimensioning in heavy goods vehicles
Geotechnical studies
Dimensioning with ALIZE

## Slide 15: Dimensioning in heavy goods vehicles
Tph(pvu) = 2 x HGV + LV
Tc = 365 x Tm x Aeq x β
Daily heavy traffic calculation | T2017 = 1922 pvu/peak hour
 | Percentage of heavy goods vehicles : 15%
 | The average daily traffic = 8 x Traffic in peak hour
Cumulative traffic | Tc = 365 x T2022 x 0.5 x 0.9 = 7, 1.10^6 axle of 13 T
We have : Tc > 4 millions so we will determine the traffic class by ”ALIZE”

## Slide 16: Geotechnical studies
Localisation de our project: zone B
α = 0,67 et β = 0,33
Soil’s class S2

## Slide 17: Geotechnical studies
30 cm
22 cm
6 cm
❶
❸
5
❷
4
20 cm
Calculation of allowable limits
The admissible vertical deformation of the soil:
The admissible horizontal deformation of the BB:
 | Soil | BB
Z, adm (def) | 361,5 | -
t, adm (def) | - | 69,2
 | Soil | BB
 | 361,5 | -
 | - | 69,2

## Slide 18: Dimensioning with ALIZE

## Slide 19: Dimensioning with ALIZE

## Slide 20: MODELING THE BRIDGE USING “SAP2000”
Data entry
Dynamic study
Studying the bridge under load "Al"

## Slide 21: Data entry
Defining the workspace
Drawing the shell
Defining the materials
Assigning the section to the shell
Calculating by finite element method
Locating the bearings

## Slide 22: Dynamic study
Dynamic study of the structure up to the 6th clean modes.
Displaying loads under the self-weight in "SAP2000“.
Frequencies obtained:

## Slide 23: Dynamic study
Parameters that influence the natural frequency of the structure
  Constant load
  Temporary dynamic load
  Other temporary loads
Solutions :
  Give the deck an inverted airplane wing profile so that, in windy conditions, it exerts a downward force instead of lifting and falling.
  Surround the cables with a profiled sheath in order to limit their drag.
  The use of shock absorbers which absorb the energy caused by the earthquake.

## Slide 24: Studying the bridge under load "Al"

## Slide 25: Studying the bridge under load "Al"
Moment on central support

## Slide 26: Studying the bridge under load "Al"
Moment at mid-central span

## Slide 27: Conclusion
Designing the interchange using “AutoCAD”.
A traffic and a geotechnical studies enabled us to size the roadway with "ALIZE".
Modeling the slab bridge by finite element method using “SAP2000”.

## Slide 28: Thank you for your attention